## Slide 1: Improving the effect of the short flows in the data center network with Multipath TCP - Multipath TCP適用時のデータセンターネットワークでのショートフローに対する影響の改善 Shogo Fujii - sekiya labratory
As the result of reproduction experiment[20],
MPTCP generates more traffic data, and causes delay with packet loss.
MPTCP has not achieved perfect effectiveness, only with 2 paths.
Hypothesis : Using uncongested path, improving the performance of short flow.
Purpose
validate the hypothesis.
figure out why negative effect for short flows happens.
Today’s requirement for large-scales cloud data center is getting higher and higher, for example web search engine and SNS(Social networking service) demands soft real-time response. Multipath TCP (MPTCP) improves throughput on modern topology which has multipath on host-to-host traffic. However, some researchers reported MPTCP affects short flow traffic negatively. In my research, I figure out why negative effect happens with two negative factors, bottleneck at aggregation switch and multiplexed flow patterns in one host.
Big data growth matters seriously …
Approach in data center
Scale-out, redundancy, cloud service
Improving datacenter network with MPTCP
MPTCP affects short flow traffic negatively[10]
Why short flow?
commonly using distributed processing application in data center
- 80% of data center traffic is short flow[16]
- Partition /Aggregate structure[3]
Short flows in datacenter network is matter
Related work : approaching for switch, protocol etc…[9, 11]
In my research –
Using modern topology for massive resources
Seamless operation : without special implementation and device
Application friendly : optimizing the specified traffic patterns
Goal : Constantly high performance datacenter network with MPTCP
Effect of link utilization and short flow interval
What happens?
1. Queue buildup-Fig7(b)
Long-lived background flow cause the length of the bottleneck queue to grow.
2. Incast-Fig7(a)
Many flows coverage on the same interface of aggregate switch over a short period of time, synchronously.
・ Impairment on the short flows:
queue-buildup delay, they are in queue behind packets from the large flows, even when no encounter with bursty traffic.
packet loss.
・Solution :
Reducing the size of the queues at aggregation switch
Outline
Background
Simulation environment
Topology : 4-node(2-pairs) FatTree like topology
Simulator : ns-3 DCE(Direct Code Execution)
Benchmark traffic
Background flow with MPTCP and 2~70KB short flow on average 200ms (poisson arivals), and measuring FCT(Flow completion time) for short flow - 1000times on simulation.
Result
Core
Aggregation
Edge
Host
Fig.1 Fat tree topology(k=2)
Exploratory approach
Validated the hypothesis from reproduction experiment, and improving the performance of short flow by selecting uncongested path.
Clarified short flow delays arise under what circumstances; Queue buildup and Incast patterns, and gave the direction for solutions.
Reproducing these problems in a real world, and proposing the method for avoiding pressuring aggregating switch queue.
Analyzing the unclear point of short flow delay, application or hardware side etc. as my future work.
Analysis
Parameter | Value
aggr-edge | 200Mbps
edge-host | 100Mbps
RTT | 0.5ms
Buffer | 50kb
Table1 : network parameter
Conclusion
14-MU
Fig.2 Simulation topology
Fig3: Flow completion time and link utilization for 70kb benchmark traffic
Fig4: 95 percentile FCT for short flow
Improvement
by10ms
Fig5: Queuing-delay by background flow
Fig6: Difference in data receiving process with flow-interval
448%
Waiting time for receiving
other flows data
Fig7: Two ways in which flows interact on a multi- ported switch resulting in performance problems.