## Slide 1: Paper 1
Title : BCube: A High Performance, Server-centric Network Architecture for Modular Data Centers
Guo, Chuanxiong, et al. Microsoft Research Asia
ACM SIGCOMM Computer Communication Review 2009

## Slide 2: Outline
Motivation
  Fault tolerant
  Load balancing
  accelerating bandwidth intensive application
Methodology
  Server-centric approach
  file systems, a file is divided into chunks, GFS etc..
  Commodity switch
  Interconnection structure
  Routing protocol

## Slide 3: Background
Bandwidth-intensive application support
  One-to-one
  One-to-several
  One-to-all
  All-to-all
Low-end commodity switches
  Low-end nonprogrammable switches
Graceful performance degradation
  Frequent component failure by commodity servers and switches

## Slide 4: BCube structure
Servers with multiple ports
Switches connecting a constant number of servers
n : number of Bcubes
k : level k

## Slide 5: Routing
n=4, k=1
Hamming distance of [00] -> [31] is 2
00, <1,0>, 30, <0,3>, 31
00, <0,0>, 01, <1,1>, 31

## Slide 6: One-to-one routing
In n=8, k =3, the path between A(0001) and B(1011)
There are h(A, B) and k+1-h(A,B) paths
  0001, < 3, 001 >, 1001,< 1, 101 >, 1011
  0001, < 1, 001 >, 0011,< 3, 011 >, 1011
  0001, < 2, 001 >, 0101,< 1, 011 >, 0111,< 3, 111 >, 1111,< 2, 111 >, 1011
  0001, < 0, 000 >, 0002,< 3, 002 >, 1002,< 1, 102 >, 1012,< 0, 101 >, 1011
These path are parallel
  Each path has unique servers and switch
Speedup

## Slide 7: Speedup for One-to-several Traffic
Edge-disjoint complete graph
the selected servers are located at different levels of BCube, thus improving replication reliability
a chunk to r chunk servers, 1/r chunk to each and copying

## Slide 8: Speedup for One-to-all Traffic
A source can split a file into k+1 path
The time to deliver a file, size L, is 1/k+1
Spaninng tree

## Slide 9: Aggregate Bottleneck Throughput for all-to-all Traffic
Bottleneck flows is receiving the smallest throughput
ABT is the number of flows times the throughput
ABT in Bcube is
the ABT of BCube increases linearly as the number of servers increases

## Slide 10: BCube Source Rooting
Without coordination of the intermediate servers
Intermediate servers do not involve in routing and just forward
Using a default path selected from the parallel path set
Failed link database

## Slide 11: Graceful degradation
Simulation –
  Bcube : n=8, k=3, 2048servers 1GB/s link
  Fat-tree : 5 layers, 0~3->512switches, 4->256switches
  Dcell : Dcell2 has 28 fullDCell1 with 32 servers
Notes: Fat-treeはパスのChoice が少ない。依存しがち。コアがやられると、劇的に減衰する。
Bcubeはロバスト性あり

## Slide 12: CPU Overhead for Packet Forwarding
5 servers as part of a BCube3
  0000, 0001, 0010, 0100, 1000
4 TCP connections
  0001 – 0100, 0010 – 1000, 0000 to all the others

## Slide 13: Prototyped the BCube
Testbed
  46 Dell Precision 490 servers
  8 8-port mini-switch
  CPU : 2GHz, 4GB DRAM
  No disk access because of the performance without disk I/O

## Slide 14: Bandwidth-intensive application support
MTU : 9KB, Sending data : 10GB
One-to-one
  00->12
One-to-several
  00->01, 10
One-to-all
  00->15 servers
All-to-all
  TCP connection with full mesh

## Slide 15: Bandwidth-intensive application support
BSR is both robust and efficient

## Slide 16: Related work
Notes: Wireの数、スループットを上げる。その分スイッチがいる。
それに伴い、コストもかかる。

## Slide 17: Future work
studying how to scale our server-centric design from the single container to multiple containers

## Slide 18: Paper 1
Title : BCube: A High Performance, Server-centric Network Architecture for Modular Data Centers
Guo, Chuanxiong, et al. Microsoft Research Asia
ACM SIGCOMM Computer Communication Review 2009

## Slide 19: Outline
Motivation
  Scalable interconnection bandwidth
  Economies of scale
  Backward compatibility
Methodology
  Approaching to architecture
  SMP(Symmetric Multiprocessing)
  MPP(Massively Parallel Processing)

## Slide 20: Simple Fat-tree