## Slide 1: Paper
Title : Longer is better: exploiting path diversity in data center networks.
Tso, Fung Po, et al. : University of Glasgow
IEEE 33rd International Conference on Distributed Computing Systems.
2013.

## Slide 2: Introduction
Motivation :
  DC network is much more centralized characteristics than the legacy Internet
  Multipath protocols, node-local and heuristic information
Methodology :
  Schedule flow over both shortest and non-shortest paths
  To mitigate the performance degradation of heavily utilized links

## Slide 3: Proposed method

## Slide 4: Proposed method
Baatdaat : a flow scheduler to reduce congestion and increase the usable capacity of DC topologies
Requirements
  A hardware-assisted traffic monitor that measures link utilization on the switches at line-speed
    without impacting their forwarding performance
  A SDN-based adaptive flow scheduling system that enforces network-wide traffic engineering based on link-local metrics
  by spreading load over shortest and detour paths, at the same time reducing flow completion time.
For short-term traffic

## Slide 5: System design & Architecture

## Slide 6: Design requirements
Each switch should be able to monitor link utilization at line rate
  NetFPGA’s OpenFlow implementation with stable line-rate throughput
Flows should be allowed to opportunistically take detours
  so long as it doesn’t impact individual flow performance.
flow scheduling should easily scale to the size of a DC network
  In order not to turn the controller into the bottleneck, the controller only determines detour paths, basically ECMP

## Slide 7: System architecture
Using multiple controllers
Multiple controllers can work independently requiring no synchronization
Each controller can interact with switches within a pod and compute pod-local paths

## Slide 8: System architecture

## Slide 9: Benefits of Hardware Implementation
Three platforms
  NetFPGA hardware
  the Open vSwitch kernel module
  the Stanford reference user-space OpenFlow implementation
Comparison the benefit of offloading work
between software and hardware implementation
Polling interval is 1ms

## Slide 10: Benefits of Hardware Implementation
Experiment:
  testbed setup was two end-host systems connected via a switch
  AMD Athlon 64 X2 5600+ systems, 3.5GB RAM and a 82571EB Gigabit Ethernet NIC installed
  NetFPGA box, AMD Phenom II X4 965 with 3.5GB RAM, a 4x1G NetFPGA, card, and a 2x1GB Intel 82571EB Gigabit Ethernet NIC
  Intel NIC was used to test the kernel and user-space implementation
10,000
back-to-back pings

## Slide 11: Benefits of Hardware Implementation
Experiment : CPU utilization
  throughput tests using Iperf with TCP and a variety of UDP datagram sizes for 60 seconds
UDP : 956Mb/s
TCP : 940Mb/s
The same throughput rates as the reference NIC
Not impact the line-rate forwarding capabilities
lower ping times, and lower CPU utilization
NetFPGA Ref. Switch does not support multipathing

## Slide 12: Measurement module design
OpenFlow v1.1 has added support for ECMP
However the reference, hardware implementation is not yet available
Baatdaat ensures that all packets belonging to the same flow due to TCP ‘s out-of-order packet

## Slide 13: Baatdaat SCHEDULING

## Slide 14: Baatdaat scheduling
Baatdaat is a flow-based scheduler
  when all links have 0% utilization, the flow is randomly scheduled using commodity ECMP
  Measurement loop to run every 1 ms with an aim to capture instantaneous traffic bursts
Aggregation switches
  need to report statistics to the controller
  The report frequency is set to 100 ms

## Slide 15: Baatdaat scheduling
Two constraints
  the flow is downlink traffic of the aggregation switches
    detours only happen between the aggregation and the Top-of-Rack
    cross-aggregation-switch traffic is more common than cross-core-switch
  the flow can only take a detour of 2 hops longer than the shortest path
    to prevent oscillation and flooding-like effects in the network

## Slide 16: Baatdaat scheduling
A link utilization matrix M, is a m×n matrix
  m : the number of aggregation switches in a pod
  n : the number of downlink ports on an aggregation switch
path diversity in the fat tree network(2 hops)
  k/2 × (k/2-1)×(k/2-1-2)
    Shortest path : k/2
The path utilization of detour paths
  max(detour links) ×c
  c : a weighting factor to reflect the fact that it is a longer path(c=1.5 works well)

## Slide 17: How does the controller determine detour paths?
Starting by constructing an acyclic tree of depth 3(using matrix M)
The time complexity of this search is
  O((k/2-1)^2)
Link2-3-4 is the actual detour determined by the controller.

## Slide 18: How does the controller determine detour paths?
Canonical tree DC topology
  every set of m switches connect to two aggregation switches
  2 × (m-1) : complexity O(m)

## Slide 19: Performance evaluation

## Slide 20: Performance evaluation
Fat tree :
  k = 8 fat-tree topology(128 servers, 8 pods amd 8switches each )
  1Gb/s interconnect links in ns-3 with the OpenFlow module
  Simulated flows consist of uniformly chosen 4 KB, 8 KB, 100 KB flows
    latency-sensitive flows common in DC networks
Target
  small flows which are mostly found in the production data mining and Web service Cloud DCs

## Slide 21: Network-wide Experimental Results
4KB
8KB
100KB
all types of flows by up to 18%
only deviates by 3% from optimal
Allowing larger number
of flows to complete faster

## Slide 22: Impact of Measurement Intervals
Baatdaat uses temporal network load to schedule network flows
  the link utilization measurement interval becomes crucial
Experiment :
  increased the measurement interval from 1 ms to 10 ms and 100 ms

## Slide 23: Impact of Measurement Intervals
4KB
8KB
100KB

## Slide 24: Impact of Measurement Intervals
Traffic flows with smaller flow size are more vulnerable to sparse measurement intervals.
Long measurement interval leads to less responsive to transient changes in network load

## Slide 25: Impact of Longer Paths
How much longer is the ideal for DC networks?
suggest that only
detours of two extra hops

## Slide 26: Testbed Experimental Results
Canonical tree topologies
  implemented Baatdaat
6 OpenFlow switches and 4 server hosts
2 aggregation switches with the controller through out-of-band connections, do not carry any data
To accurately capture DC network characteristics, oversubscription ratio of 1 : 5, from 1 Gb/s to 100 Mb/s

## Slide 27: Testbed Experimental Results

## Slide 28: Baatdaat Overhead
In Baatdaat
  the control message overhead would be attributed to
    8 × 48 = 384 Bytes (assuming a 48 port switch)
  384000 Byte/sec
This is a marginal cost, for improving flow completion times.

## Slide 29: Hardware Implementation Complexity

## Slide 30: Controller Efficiency
How many flows the controller can handle at a time?
The controller runs on a machine with an Intel i5 2.3Ghz CPU and 4GB RAM

## Slide 31: Related work
ECMP suffers from hash collisions, which can result in unbalanced flow allocations
  Valiant Load Balancing(VLB) to randomize packet forwarding
    VL2, Monsoon
DeTail
  using flow priorities
Dcell, SPAIN
  Modifications to end-hosts are required
DevoFlow
  replace the OpenFlow model

## Slide 32: Conclusion
Baatdaat, a novel flow scheduling system for DC networks
Using a modified NetFPGA implementation of OpenFlow to directly measure the temporal network-wide utilization
Using shortest and non-shortest paths
Unlike existing flow scheduling, Baatdaat uses the current state of the network dynamically
Reducing network-wide maximum link utilization by up to 18%
Reducing flow completion times by up to 10%