## Slide 1: Paper
Title : DeTail: Reducing the flow completion time tail in datacenter networks
Zats, David, et al. University of California, Berkeley, Berkeley
ACM SIGCOMM Computer Communication Review 2012

## Slide 2: Outline
Motivation :
  Reducing the tail of
    completion times
    latency-sensitive flows critical for page creation
Methodology :
  Cross-layer
  In-network mechanisms to reduce packet losses and retransmissions
  Prioritize latency-sensitive flows
  Evenly balance traffic across multiple paths

## Slide 3: introduction

## Slide 4: Problem of current DC network
Background
  Modern Web pages are made up of many components
    generated by independent subsystems and “mixed”
    “subflow”:intra-datacenter flow is increased
    Partial delay
  Deadlines are 200 -300ms for satisfaction for user demands
Purpose:
  reducing the long flow completion tail

## Slide 5: Problem of current DC network
Flow completion times
  depend on round-trip-times(RTTs)
  Congestion affects performance
    DC RTTs is as low as 250µs, while they grows by two orders of magnitude[1]
Each contributes to increasing the long tail of flow completion(congestion)
  Traffic bursts cause packet loss and retransmissions
  Uneven load balancing causes high congestion for subflow
  The absence of traffic prioritization causes to wait latency-sensitive flows
[1] ALIZADEH, M., GREENBERG, A., MALTZ, D. A., PADHYE, J., PATEL, P.,PRABHAKAR, B., SENGUPTA, S., AND SRIDHARAN, M.
Data center tcp(dctcp). In SIGCOMM (2010).

## Slide 6: Problem of current DC network
Solution : detecting flash congestions
Proposed method : Detail
  Quantification of the impact of long-tailed flow completion times
  Assessment of the causes of long-tailed flow completion times
  A cross-layer network stack that addresses them
On simulation, reducing 99.9th percentile flow completion time

## Slide 7: Analysis of long tail

## Slide 8: Long-tail flow
Intra-rack RTTs take 61µs as average, and the median is 334µs
In 10% of the cases, average RTTs take 14ms
Worker
Mid-level aggregator
Top-level aggregator
Rack

## Slide 9: Web workloads
Partition-Aggregate
Sequential
“Normal” : the normal distribution having a 50% higher median than the measured one
If RTT follows the Normal, no worker missed the deadline
Long-tail flow is critical

## Slide 10: Cause of long tails
Flash congestion have three problems leading to long-tailed flow completion time
  packet losses and retransmissions
  absence of prioritization
  uneven load balancing

## Slide 11: Packet losses and retransmissions
Packet losses often lead to flow timeouts
  In DC, timeouts are set to 10[ms]
  Datacenter RTTs are commonly 250μs
  Just one timeout guarantees that the short flow will hit the long tail (tradeoff between timeout and page creation)
  Multiple workers respond to the same aggregator
    correlated losses and timeout hitting the long tail

## Slide 12: Absence of prioritization
There are both latency-sensitive and latency-insensitive flows, with the range from 2KB to 100MB
In case,
  short latency-sensitive flows can become enqueued behind long latency-insensitive flows
  latency-sensitive flows will hit the long tail
Notes: datacenters must support both latencysensitive and latency-insensitive flows, with sizes that typically range from 2KB to 100MB

## Slide 13: Uneven load balancing
Modern DC networks have scaled out, creating many paths
Two static approaches
  Flow hashing : Imperfect hashing, as well as varying flow sizes often lead to uneven flow assignment
  Packet scatter : randomly picks the output ports for using multiple paths

## Slide 14: Uneven load balancing
In asymmetries, they can’t be adaptive
  Asymmetry : incremental deployment or network reconfigurations
・Simulation :
128-servers FatTree topology
Oversubscription : ½ × ½
All-to-all workload, 2KB, 8KB,32KB
100Mbps : link of core-aggregate

## Slide 15: Related work
DCTCP. D3, and HULL
  single path solutions : fairness and congestion control
  No uneven load balancing
Hedera
  Monitoring link state and remap flows
  Takes more costs : remap per 5sec and using 10% of link capacity
MPTCP
  Multiple TCP subflows and balances traffic based on congestion
  Using standard TCP congestion detection mechanisms
  Effective for flow sizes larger than 70KB
  The flow more than 10packets

## Slide 16: Problem of these solutions
Trend : to minimize in-network functionality
  host-based or controller-based approaches
Critical factor
  Quick response times are needed to support latency-sensitive flows
Network-oriented approach

## Slide 17: Proposed method

## Slide 18: Proposed method : Detail
Detail is ..
  Cross-layer network-based approach for reducing the long flow completion time tail

## Slide 19: Assumed switch architecture
Combined Input/Output Queue(CIOQ) Switch
IP Lookup : Forwarding engine
Ingress/Egress queue : buffer
Drain byte counter : monitor of buffer
CIOQ architecture is commonly used in today’s switch

## Slide 20: Link layer
Lossless fabric :
  the switch monitors ingress queue occupancy to detect congestion
  When the drain byte counters of an ingress queue pass a threshold, the switch send Pause message to previous hop

## Slide 21: Network Layer
Congestion-based load balancing decisions
  Picking an acceptable port with the smallest drain byte counter at egress queue
  Setting threshold for saving computational cost
    By reacting to local egress queue occupancies, making globally-aware hop-by-hop decisions without additional control messages(PAUSE)
  Adaptive load balancing
    Setting multiple thresholds for priorities

## Slide 22: Network Layer
Detail choose randomly one of multiple ports
To obtain the set of lightly loaded ports

## Slide 23: Transport Layer
Load balance
  Packet drops no longer happen due to congestion.
  When the appropriate counter is above a threshold, and low priority packets enqueued, setting ECN FLAG
Lossless fabric
  Standard TCP
    Reaction to out-of-order packet delivery
Notes: Low priority packets enqueued when the appropriate counter is above a threshold have their ECN flag set

## Slide 24: Application layer
DeTail depends upon applications to properly specify flow priorities based on how latency-sensitive they are
At Detail, using only two priorities
Notes: DeTail depends upon applications to properly specify flow priorities based on how latency-sensitive they are

## Slide 25: Choice of settings

## Slide 26: Choice of settings
Choosing the parameters of Detail’s mechanisms
Link layer flow control : triggering PFC (Priority flow control) messages
Adaptive load balancing : threshold
Explicit Congestion Notification(ECN)
End-host timers : timeout

## Slide 27: Link layer flow control
For 1GibE, 128KB buffers and eight priorities
  Unpause threshold (min) : 4557 Drain Bytes
  Pause threshold (min) : 8192 Drain Bytes
The time to generate PFC message is 36.456µs for 4557B
131072B(128KB)/8 – 4557 = 11827B (maximum)
8192B(halfway between the minimum and the maximum)
Notes: halfway between the minimum and the maximum

## Slide 28: Adaptive load balancing
When performing threshold-based adaptive-load balancing, we must determine how many thresholds to have for a given priority
In this simulation,
  Setting two threshold 16KB and 64KB

## Slide 29: Explicit Congestion Notification(ECN)
Threshold of 64KB drain bytes
Tradeoff(ex.
  Setting too low, reducing the likelihood of head-of-line blocking, but increases the chance that low-priority flows will back off too much

## Slide 30: End-host timers : timeout
Setting the timeout duration of end host timers too low may lead to spurious retransmissions that waste network resources.
In simulation,
  We saw that values of 10ms and higher effectively avoid spurious retransmissions
  DC topologies typically have multiple hops, so 200ms as RTOmin

## Slide 31: experiment

## Slide 32: Experimental setup
NS-3 Simulation
  ingress and egress queues of 128KB buffers per port
  Switch delays : 25μs
    12.24μs transmission delay of a full-size 1530B Ethernet frame on a 1GigE link.
    3.06μs crossbar delay
    0.476μs propagation delay
    5μs transceiver delay
    4.224μs forwarding engine delay

## Slide 33: Experimental setup
Click-based implementation
  Modifying Click to have both ingress and egress queues
  Implementing DMA(Direct Memory Access) etc..

## Slide 34: (1)microbenchmarks
FatTree with 128servers
Four pods
Four Tor switches
Four aggregate switches
Oversubscription : ½ × ½
The data retrievals follow a Poisson process
Rates ranging from 500 to 2000
All-to-all:Each server randomly selects another server
FH (b): 6.3~7.3ms
Detail (b):2.1~2.3ms
The worsts are 2.6ms and 28ms

## Slide 35: (1)microbenchmarks

## Slide 36: (1)microbenchmarks
Front-end/Back-end:
Each server in first three pods (i.e, front-end server) retrieves data from a randomly selected server in the fourth pod (i.e., back-end server)
30%~65%

## Slide 37: (1)microbenchmarks
16-server FatTree
300 retrievals/sec
The background flows are 1MB, 16MB or 64MB
38~60% reducing

## Slide 38: (2)Topological asymmetries
Disconnected Link
One disconnected aggregate-to-core link
LPS(Lossless Packet Scatter):packet scatter with Priority Flow Control, not including Adaptive Load Balancing
At 2000 retrievals, almost an order of magnitude improvement(18ms and 159ms)

## Slide 39: (2)Topological asymmetries
Degraded Link
Core-to-agg link can be downgraded from 1Gbps to 100Mbps
More than 91% reduction compared to FH by redirecting traffic to alternate paths(ALB)
under FH and LPS was more than 755ms
37ms under DeTail

## Slide 40: (3)Workload
Sequential : 38ms ~ 18ms
Partition : 17ms(40 servers)
Deadline : 200~300ms

## Slide 41: Conclusion
Avoiding congestion leads to reduction of flow completion time, not hitting long-tail(10%)
Proposed method : Detail
  Cross-layer approach
  In-network mechanisms to reduce packet losses and retransmissions
  Prioritize latency-sensitive flows
  evenly balance traffic across multiple path
DeTail can reduce 99.9th percentile flow completion times by over 50% for many workloads.