## Slide 1: Improving Datacenter network with MPTCP
Sekiya Lab.
M1 Fujii Shogo

## Slide 2: Introduction
Background
  Modern Web pages are made up of many components
    generated by independent subsystems and “mixed”
    “subflow” : intra-datacenter flow is increased
    Partial delay
  Growing the number of hosts per DC
  Deadlines are 200 -300ms for satisfaction for user demands
A approach for DC topology
  Replacing traditional hierarchical structure
  FatTree, Bcube and VL2 etc…

## Slide 3: A approach for DC topology
These topologies take advantage to distributed processing
Basically, multiple paths are for redundancy
Multipath TCP
Tree Topology
(Traditional)

## Slide 4: What is MPTCP?
MPTCP :
  An ongoing effort of the IETF's Multipath TCP working group
  The aims at allowing a TCP connection to use multiple paths to maximize resource usage and increase redundancy
For Datacenter
  Paper : “Improving datacenter performance and robustness with multipath TCP”
  Raiciu, Costin, et al., University College London
  ACM SIGCOMM Computer Communication Review. Vol. 41. No. 4. ACM, 2011

## Slide 5: Benefit of MPTCP
With eight subflows, most MPTCP flows get at least
90% of the available capacity
Benefit for Long-lived flow
FatTree topology, 128(80-eight port switch) and 8192 nodes, and 100Mb/s links
Packet-level(htsim), Flow-level simulators
Show the aggregate throughput achieved by long-lived TCP and MPTCP

## Slide 6: The current problem of MPTCP 1/2
Effective for flow sizes smaller than 70KB
Algorithm | Short Flow Finish Time(mean/stdev) | Network Core Utilization
SINGLE-PATH TCP | 78 ±108 ms | 25%
MPTCP | 97 ± 106 ms | 62%
Compared to TCP, MPTCP increases mean completion time by 25%
MPTCP’s lower aggressiveness and better load balancing greatly reduce impact on competing traffic
FatTree topology, 128nodes, 4:1oversub
Sending 70KB file on average 200ms(poisson arrivals)
Using 33% of nodes by 1 to 1traffic

## Slide 7: The current problem of MPTCP 2/2
The flow less than 10packets
Most of flows are better for MPTCP
The flows less than 10 packets are not effective for MPTCP
FatTree topology, 128nodes, 4:1oversub
File size(pkt) is changed
Showing that a Download time with TCP and MPTCP

## Slide 8: My research
Topic
  Improvement the completion time of short flow in FatTree with MPTCP
Target
  Flow : Less than 70KB or 10 packets flow
  Network: DC network FatTree
Goal
  Improving 99.9th percentile flow completion time within 300ms by MPTCP than TCP
  The solution for not only long-lived but short-lived flow

## Slide 9: Related Work 1/2
Packet scatter : improving for short flow
  per-packet load balancing with round-robin ECMP
  a single congestion window as it is unaware of the multiple paths
Paper
  “Improving datacenter performance and robustness with multipath TCP”
  Raiciu, Costin, et al., University College London
  ACM SIGCOMM Computer Communication Review. Vol. 41. No. 4. ACM, 2011

## Slide 10: The current problem of MPTCP 1/2
Effective for flow sizes larger than 70KB
Algorithm | Short Flow Finish Time(mean/stdev) | Network Core Utilization
Packet Scatter | 42 ± 63 ms | 30%
MPTCP | 97 ± 106 ms | 62%
Compared to MPTCP, Packet Scatter can finish short flow faster
About core utilization, Packet Scatter gets low utilization
FatTree topology, 128nodes, 4:1oversub
Sending 70KB file on average 200ms(poisson arrivals)
Using 33% of nodes by 1 to 1traffic

## Slide 11: The current problem of MPTCP 1/2
Individual link loss rates
FatTree topology, 128nodes,
running a permutation traffic matrix of long flows
At access link, Packet Scatter is worst rate
  Because of fine-grain control, per-packet round-robin
  Constraint its transmit rate

## Slide 12: Update : Q at the last meeting
In DC, there are short message(50KB~1MB) uploading control state and long background flows(5KB~50MB) providing fresh data
DC have a diverse a mix of flows with widely varying deadlines
Wilson, Christo, et al. "Better never than late: Meeting deadlines in datacenter networks." ACM SIGCOMM Computer Communication Review. Vol. 41. No. 4. ACM, 2011.

## Slide 13: Future Work
論文でのシナリオの再現[1]
  70KB以下のflow, 10パケット以下のflowに対して, TCPよりも性能が悪いのかどうかの確認, その原因に関する解析
[1]Alizadeh, Mohammad, et al. "Data center tcp (dctcp)." ACM SIGCOMM Computer Communication Review 40.4 (2010): 63-74.
[2] Raiciu, Costin, et al. "Improving datacenter performance and robustness with multipath TCP." ACM SIGCOMM Computer Communication Review. Vol. 41. No. 4. ACM, 2011.
解析の掘り下げ(3シナリオ[2])
  a) Incast : 2KB(2 packets)のflowを複数流す.
  - Short Flowに対するMPTCPのオーバヘッドの影響
  b) Queue buildup : Long Flow + Short Flow(20KB) を同じOutput Portへ流す
  - Long Flowのセットアップのオーバヘッドの影響
  c) Buffer pressure : Long Flow + Short Flow(20KB) を異なるOutput Portへ流す
  - スイッチ内のバッファへの影響

## Slide 14: 3シナリオ

## Slide 15: About the solution…
MPTCP : static approach
Dynamic approach
  Data Center TCP(DCTCP) : Dynamic Bufferng
      Alizadeh, Mohammad, et al. "Data center tcp (dctcp)." ACM SIGCOMM Computer Communication Review 40.4 (2010): 63-74.
  Monitoring the sample packet (1/7)th, is queue size
  Exceeding the threshold queue size, changing buffer
  Optimizing OpenFlow
      http://mptcp.info.ucl.ac.be/
  Getting rid of collision

## Slide 16: TCP in data centers
      http://mptcp.info.ucl.ac.be/

## Slide 17: TCP in FAT tree networks Cost of collissions
C. Raiciu, et al. “Improving datacenter performance and robustness with multipath TCP,” ACM SIGCOMM 2011.

## Slide 18: How to get rid of these collisions ?
Consider TCP performance as an optimisation problem

## Slide 19: Related Work 2/2
“Detail” : improving flow completion time
  Cross-layer approach
  In-network mechanisms to reduce packet losses and retransmissions
  Prioritize latency-sensitive flows
  Evenly balance traffic across multiple paths
Paper :
  Title : DeTail: Reducing the flow completion time tail in datacenter networks
  Zats, David, et al. University of California, Berkeley, Berkeley
  ACM SIGCOMM Computer Communication Review 2012

## Slide 20: Long-tail flow
Intra-rack RTTs take 61µs as average, and the median is 334µs
In 10% of the cases, average RTTs take 14ms
Worker
Mid-level aggregator
Top-level aggregator
Rack

## Slide 21: Cause of long tails
Flash congestion have three problems leading to long-tailed flow completion time
  packet losses and retransmissions
  absence of prioritization
  uneven load balancing

## Slide 22: Experimental setup
Click-based implementation
  Modifying Click to have both ingress and egress queues
  Implementing DMA(Direct Memory Access) etc..

## Slide 23: Absence of prioritization
There are both latency-sensitive and latency-insensitive flows, with the range from 2KB to 100MB
In case,
  short latency-sensitive flows can become enqueued behind long latency-insensitive flows
  latency-sensitive flows will hit the long tail
Notes: datacenters must support both latencysensitive and latency-insensitive flows, with sizes that typically range from 2KB to 100MB

## Slide 24: Transport Layer
Load balance
  Packet drops no longer happen due to congestion.
  When the appropriate counter is above a threshold of drain byte, and low priority packets enqueued, setting ECN FLAG
In this simulation,
  Setting two threshold 16KB and 64KB
Notes: Low priority packets enqueued when the appropriate counter is above a threshold have their ECN flag set

## Slide 25: microbenchmarks
FatTree with 128servers
Oversubscription : ½ × ½
All-to-all:Each server randomly selects another server
8KB data retirvals under all-to-all workload of 2000 retrievals /sec
Flow Hashing (FH) (b): 6.3~7.3ms
Detail (b):2.1~2.3ms
The worsts are 2.6ms and 28ms

## Slide 26: 研究計画
短期
  MPTCP + FatTree Helper on ns-3
  Inspection of the influence by short-lived flow
中期
  10~12月-融合情報コース成果発表
  2013年12月19日-ネットワークシステム研究会
    モバイル、アドホック、ユビキタス、無線、セキュリティ、マルチアクセス、アクセスネットワーク・User Network Interface、Homeネットワーク、一般
  2014年1月:発表会

## Slide 27: ns-3 – status quo
Setup Ns3-dce -- finish
Creating FatTree topology(128 nodes) -- finish
Configuring routing table -- 70%
Making scenario by “iperf”
Analyzing

## Slide 28: Future work
Completing more than 1 scenario by ns-3
  Deadline 11th
Reading RFC of MPTCP
実機も動かせるように・・小さいトポロジー
  あくまでシミュレーション