## Slide 1: Improving Datacenter network with MPTCP
Sekiya Lab.
M1 Fujii Shogo

## Slide 2: Background
Explosive increase in the amount of data year after year.
  the amount is doubled by 18-24months[1]!
  the storage of Facebook has more than 300 petabytes data[2].
  analyze 1 petabytes data for mining everyday.
    Soft real-time application: Web search, recommendation system, retail, etc.
Increasing also the number of hosts in a data center.
In order to bring out the best performance,
  Application approach : distributed computing.
  Physical approach : network topology
  Protocol approach : Multipath TCP
[1] http://www-06.ibm.com/systems/jp/storage/column/backup/01.html
[2] https://www.facebook.com/notes/facebook-engineering/presto-interacting-with-petabytes-of-data-at-facebook/10151786197628920

## Slide 3: Network topology
Maximally utilization of bandwidth without special devices
Multi-paths at the host-to-host traffic
traditional hierarchy topology
not efficient for modern traffic
not appropriate for the assignment of bandwidth
intra-detacenter traffic

## Slide 4: Distributed computing
The purpose is to partition the tasks and parallel computing for the scalability
ex. Presto(2013) based on Hadoop Framework
client
coordinator
worker
worker
worker
worker
worker
worker
worker
Task
scheduling
Query
Parser
Aggregate
Aggregate
Partition-aggregate model is common
Installed in interactive response and file storage servers
burst-query

## Slide 5: Protocol approarch
Multipath TCP is released in 2011.
  To increase the resilience of the connectivity by providing multiple paths, protecting end hosts from the failure of one.
  To increase the efficiency of the resource usage, and thus increase the network capacity available to end hosts.
Some researches reported MPTCP could upgrade more performance of network than existed TCP

## Slide 6: Related work(1)
“Improving datacenter performance and robustness with multipath TCP”(2011)
Algorithm | Short Flow Finish Time(mean/stdev)
SINGLE-PATH TCP | 78 ±108 ms
MPTCP | 97 ± 106 ms
In FatTree, MPTCP is installed and improving throughput.
For short-flow(70KB), MPTCP is not effective
average completion time in 70KB-flow
[1]Raiciu, Costin, et al. "Improving datacenter performance and robustness with multipath TCP." ACM SIGCOMM Computer Communication Review. Vol. 41. No. 4. ACM, 2011.
[1]
[1]

## Slide 7: Related work(2)
DeTail: Reducing the flow completion time tail in datacenter networks. (2012)
Observing the traffic on cross-layer, and rearranging the queue
overall short-flow is improved
However, they implemented the special switch
Assumption : Short-flow is made to be behind the long-flow, and leading to delay.
[1]Zats, David, et al. "DeTail: Reducing the flow completion time tail in datacenter networks." ACM SIGCOMM Computer Communication Review 42.4 (2012): 139-150.
[1]
[1]

## Slide 8: Motivation
Assumption :
  Improving performance in today’s data centers with Multipath TCP(MPTCP) by solving short-flow problems
Problems :
  MPTCP can work long-sized flow effectively
  However, for short-flow, MPTCP does not.
Simulating reproduction of related works by ns-3
Analyzing the cause of deterioration of the performance

## Slide 9: Requirements
3-requirements,
  using the modern topologies for utilization massive computing resources.
  improving the short-flow for the burst queries by distributed computing.
  seamless approach : not using the specialized devices, but utilizing the existing resources.
My solution,
  FatTree topology
  Targeting on solving the problem of short-flow keeping the performance of long-flow
  Using MPTCP on FatTree

## Slide 10: Is our target critical?
The requirements for today’s application is severe
  Applications have to meet SLA is 200-300[ms], or ship out user reply.
    additional latency of 100[ms] costs Amazon 1% of sales[1]
  80% of the flows are smaller than 10KB in today’s datacenter[2].
[1]Wilson, Christo, et al. "Better never than late: Meeting deadlines in datacenter networks." ACM SIGCOMM Computer Communication Review. Vol. 41. No. 4. ACM, 2011.
[2]Benson, Theophilus, Aditya Akella, and David A. Maltz. "Network traffic characteristics of data centers in the wild." Proceedings of the 10th ACM SIGCOMM conference on Internet measurement. ACM, 2010.

## Slide 11: Multipath TCP
Multipath TCP extends TCP so that a single connection can be striped across multiple network paths.
server
client
Relay

## Slide 12: Multipath TCP
Better aggregate throughput
Better load balancing
Better robustness
Receiving each ACK
Packet loss
:window size of subflow r
:Sum of window size
:aggressiveness
Congestion control:
Multipath TCP in data center
Speed of window update is improved
fairness in bottleneck

## Slide 13: Traffic patterns in today’s DC
As long as application follows partition/aggregate model, the traffic patterns is classified by data plane and control plane.
Data plane
  Background traffic
    For providing fresh date to the worker.
Control plane
  query traffic
    the command for the worker from the master
  Short message traffic
    update the control state

## Slide 14: Traffic patterns in today’s DC
[1]Alizadeh, Mohammad, et al. "Data center tcp (dctcp)." ACM SIGCOMM Computer Communication Review 40.4 (2010): 63-74.
Crowd application is based on partition/aggregate model.
Therefore, the traffic patterns is classified by three patterns[1].
 | plane | frequency | size | deadline | metric
Background traffic | data | sec order | 1MB-50MB | no | throughput[bytes/sec]
Short message | control | sec-msec order | 50KB-1MB | yes | flow completion time[sec]
Query traffic | control | msec-µsec order | 2KB-50KB | yes | flow completion time[sec]

## Slide 15: Simulation for reproduction
Repdoducing “Improving datacenter performance and robustness with multipath TCP ” scenario.

## Slide 16: Topology
Benchmark traffic on FatTree.
  4:1 oversubscribed, one-to-one traffic
  33% node : background flow by MPTCP or TCP, remaining nodes : 70KB data sending by TCP
host
edge
Aggregate
core
Backgroung flow (TCP or MPTCP)
Short flow (TCP)

## Slide 17: Topology
host
edge
Aggregate
core
host
edge
aggregate
aggregate

## Slide 18: Evaluation
The peak is the almost same.
Becoming long flow is effecting the performance
Chart: フロー完結時間[ms]
[1]Raiciu, Costin, et al. "Improving datacenter performance and robustness with multipath TCP." ACM SIGCOMM Computer Communication Review. Vol. 41. No. 4. ACM, 2011.
Algorithm | Short Flow Finish Time(mean/stdev)
SINGLE-PATH TCP | 78 ±108 ms
MPTCP | 97 ± 106 ms
Algorithm | Short Flow Finish Time(mean/stdev)
SINGLE-PATH TCP | 82 ±54 ms
MPTCP | 95 ± 68 ms

## Slide 19: Simulation
We simulated FatTree with MPTCP on ns-3
Assumption application
  distributed computing
  3-traffic patterns
    Background traffic
    Query traffic
    Short message
environmental parameter | value
nodes | 16
Multipath TCP | v0.86
Bandwidth – core-aggr | 400Mbps
Bandwidth – aggr-edge | 200Mbps
Bandwidth – edge-node | 100Mbps
RTT | 0.5ms
Window size | 100KB

## Slide 20: Topology
host
edge
Aggregate
core
master
worker
Backgroung flow (TCP or MPTCP)
Short flow (TCP)

## Slide 21: Query traffic
without background
  100% master-worker traffic 200ms Poisson generate
with background
  100% master-worker traffic 200ms Poisson generate
  static long flow

## Slide 22: Query traffic

## Slide 23: Query traffic

## Slide 24: Query traffic
For less than 50KB traffic,
  MPTCP behave like TCP with single-path.
With Background traffic,
  MPTCP used wider bandwidth for background traffic, and pressure query traffic.

## Slide 25: Short message
Short message traffic without background
  50% master-worker traffic 0.5s Poisson generate
Short message traffic with background
  50% master-worker traffic 0.5s Poisson generate
  static long flow

## Slide 26: Short message
Short message traffic without background

## Slide 27: Short message
Short message traffic with background

## Slide 28: Short message
For pure performance,
  For more longer flow, MPTCP works well
With background,
  Load balancing by MPTCP improve the performance

## Slide 29: Conclusion
Verifying the performance of MPTCP in the FatTree topology
Modern intra-datacenter traffic
  Background traffic
  Short message traffic(time-sensitive)
  Query traffic(time-sensitive)
    Burst-traffic
For too short sized flow(up to 70KB), MPTCP behaves like TCP, single-path.
With background traffic, MPTCP’s fairness problem.

## Slide 30: Solution – via Core
10.33.0.1
10.33.0.2
10.32.1.1
10.32.1.2
Achieving 4-paths
10.32.0.1
10.32.0.2
10.33.1.1
10.33.1.2

## Slide 31: Solution – via Core
10.33.0.1
10.33.0.2
10.32.1.1
10.32.1.2
10.32.0.1
10.32.0.2
10.33.1.1
10.33.1.2