## Slide 1: Progress report 進捗報告
Sekiya laboratory M1
Fujii Shogo

## Slide 2: Constructing experiment environment
VM0
Experiment environment for MPTCP on KVM
VM2
VM3
VM1
VM4
Progress
  Creating five VMs
Future work
  Connecting each VMs with bridge
OS

## Slide 3: Related work
Problem : First-in-first-out mechanism harm the flow with high priority, and it misses deadline.
Solution :
  Priority-based packet scheduling
  Uncoupled rate-control
Alizadeh, Mohammad, et al. "pFabric: Minimal Near-Optimal Datacenter Transport." (2013) ACM SIGCOMM.

## Slide 4: Priority-based packet scheduling
Dequeue : For the flows with the same tuple, ordering based on priority.
Priority rule : smaller remaining flow size has higher priority.
the flow that transmits earlier is made to finish earlier
Queue size sets smaller considering overhead comparator

## Slide 5: Priority-based packet scheduling
Packet drop :
When a packet arrives to a port with a full buffer…
  if it has priority less than or equal to the lowest priority packet in the buffer, it is dropped.
  Otherwise, the packet with the lowest priority is dropped to make room for the new packet.
The flow with low priority is harmed with existing congestion control
sending out high priority flow for RTO

## Slide 6: Uncoupled rate-control
Existing rate-control :
  setting rate considering utilization of bandwidth
    slow-start, allocating initial window…
Proposed method
  Initial window size : static value using BDP
  when drop, waiting for RTO; no fast retransmits, dupACKs or any other such mechanisms
the flow dropped exposes high penalty

## Slide 7: Simulation methodology
Simulation environment
  Topology : FatTree 144hosts through 9 racks
  Protocol : ECMP with round-robin
  Simulator : ns-2
Benchmark traffic
  using real distribution

## Slide 8: Result
pFabric achieves near-optimal flow completion times for all flow sizes

## Slide 9: Result

## Slide 10: Comparing the method of prioritize
BytesSent : sending total bytes
Flow size
Remaining flow size
BytesSent : prioritize long flow

## Slide 11: Considering
目標 : 並列分散処理速度を上げる
優先度を使うにしろ、どれを使えば?
高いペナルティ : 再送処理を行わず、タイムアウトまで待たせる。
レート制御 : 既存のTCPを用いない…

## Slide 12: Future work
実装
  仮想環境での2サーバ、2ルータの設定。サーバ周り勉強
  Linux TCP/IPの勉強
論文
  Traffic engineering、MPTCP
データ取得
  Hadoop等ので分散処理させたときの分布をとってみる