## Slide 1: Progress report 進捗報告
Sekiya laboratory M1
Fujii Shogo

## Slide 2: Constructing experiment environment
Experiment environment for on Mininet
router1
router2
Host1
Host2
Progress
  Installing mininet, and testing some codes
  Trying to test the script from CoNEXT’s paper
  Studying SSH, VM
Future work
  Fixed MPTCP on mininet

## Slide 3: Related work
Problem : Utilizing effectively multiple equal-cost paths
  ECMP : deciding the flow’s route by hashing 5-tuple, cannot prevent the occurrence of hot-spot
  MPTCP : connection establishment complexity for short flow
Solution : switch based
  Random Packet Spraying(RPS)
  Simple active queue management scheme; Selective Random Early Discard(SRED)
Dixit, Advait, et al. "On the Impact of Packet Spraying in Data Center Networks." Proc. of INFOCOM. 2013.

## Slide 4: RPS Overview
RPS Overview
  Using all the equal-cost shortest paths between every source and destination pair.
  Instead of hashing, RPS spreads all packets to the shortest paths equally
Concern
  Fast retransmit : some amount of reordering can happen, but the sender wait for 3 duplicate ACK in newer Linux kernel.
  Congestion window : even if the congestion window becomes half, total aggregate performance is better than ECMP
Implementation
  On NetFPGA, using a random number provided by NetFPGA libraries.

## Slide 5: Evaluation RPS
Testbed configuration
  Fat-tree : 4-ary, 1Gbp link
  Servers : 4GB RAM, Intel Xeon(2.4Ghz)
  Oversub:1:1, 4:1, 8:1(bottom link :125Mbs )
Evaluation for long flow
  MPTCP suffers in rate-limiting
    Quality of MPTCP version?
  RPS : achieving high throughput with
  small variance

## Slide 6: Analysis of Packet Spraying
Dupacks
  Reordering will be limited because all paths between a pair of hosts have similar latencies.
  Latencies are largely determined by queue lengths.
RPS improves throughput of long flow, but not effective for short flow

## Slide 7: ASYMMETRY
In the real world, a data center network may not be symmetric at all times.
What asymmetric? : link/switch failure or link degradation
Problem illustration
500Mbps
↓
155Mbps

## Slide 8: ASYMMETRY
Effect of queue length
  In free buffer size, unrestricted buffer,
  just 17 % of throughput
  Reducing buffer sizes reduces queue
  length difference, and 35% throughput
  For high throughput, queue length difference gets lowers

## Slide 9: Keeping Queue Lengths Equal
Existing solution : Random Early Discard(RED)
  RED probabilistically drops packets as soon as the queue length crosses some threshold.
  However, the total throughput is reduced as well
Proposed method : Selective RED
  RED just for flows that induce a queue length differential.
    That flow does not use all paths for link failure.
  Using packet marking and a topology aware centralized fault manager

## Slide 10: ASYMMETRY
SRED improves total throughput comparing with RED
In link failure, RED algorithm works
MPTCP remains almost unaffected by the link failure as expected.
FatTree : 4:1oversubscribed
RED :
  Threshold_max = 20
  Threshold_min = 10
  P_max = 0.1

## Slide 11: Considering
スイッチベースのアプローチ
  MP-TCP requires significant end-host protocol stack changes, it is not always feasible in all environments, especially in public cloud platforms where individual tenants control the OS and the network stack
ランダムで散らす：単純な機構
  エンドホストだけで実現するには。。
リンクエラーが生じたときの評価
バッファサイズは大きければいいわけではない
  Modern data center operators try to keep queue lengths to the minimum to keep end-to-end latencies low and predictable

## Slide 12: Future work
実装
  仮想環境での2サーバ、2ルータでMPTCP。
  Linux TCP/IPの勉強
データ取得
  Hadoop等ので分散処理させたときの分布をとってみる
論文
  Traffic engineering、MPTCP。
  エンドホストへのアプローチ