## Slide 1: Progress report 進捗報告
Sekiya laboratory M1
Fujii Shogo

## Slide 2: Constructing experiment environment
Experiment environment for on Mininet
Switch1
Switch2
Host1
Host2
Progress
  Installing mininet, and testing some codes
  Try to create topology and POX
  MPTCP on mininet from CoNEXT’s paper
Future work
  Fixed MPTCP on mininet
  Learning OpenFlow controller
Controller

## Slide 3: Related work
MPTCP concept
  An MPTCP connection begins similarly to a regular TCP connection.
  If extra paths are available, additional TCP sessions(subflow) are created on these paths.
Ford, Alan, et al. "TCP extensions for multipath operation with multiple addresses." IETF MPTCP proposal-http://tools. ietf. org/id/draft-ford-mptcp-multiaddressed-03. txt (2011).

## Slide 4: Initiating an MPTCP Connection
Negotiating of MPTCP_capable in 3-handshake
  And also carry the MP_CAPABLE option
Host A
Host B
MP_CAPABLE
[A’s key, flags]
MP_CAPABLE
[B’s key, flags]
ACK + MP_CAPABLE
[A’s key, B’s key, flags]

## Slide 5: Initiating an MPTCP Connection
Negotiating of MPTCP_capable in 3-handshake
  And also carry the MP_CAPABLE option
Host A
Host B
SYN + MP_CAPABLE(keyA)
Addr A1
Addr A2
SYN/ACK + MP_CAPABLE(keyB)
ACK + MP_CAPABLE(keyA, keyB)
SYN + MP_JOIN(tokenA, R-A)
SYN/ACK + MP_JOIN(HMAC-B, R-B)
ACK + MP_JOIN(HMAC-A)
ACK

## Slide 6: Initiating an MPTCP Connection: detail
Initiating option is used to declare the 64-bit key, for authentication

## Slide 7: Starting a new subflow
Further subflows can be added to the connection.
Host B
SYN + MP_CAPABLE(keyA)
Addr A1
Addr A2
SYN/ACK + MP_CAPABLE(keyB)
ACK + MP_CAPABLE(keyA, keyB)
SYN + MP_JOIN(tokenA, R-A)
SYN/ACK + MP_JOIN(HMAC-B, R-B)
ACK + MP_JOIN(HMAC-A)
ACK
Host A

## Slide 8: Starting a new subflow: the other way
Path management: to the exchange of information about additional paths between hosts.
As the second method, ADD_ADDR option
  signals addresses explicitly to the other host to allow it to initiate new subflows
  support operation through NATs

## Slide 9: Starting a new subflow: the other way
Operation: after setup A1-B1
Addr A1
Addr A2
Host A
Addr B1
Addr B2
Host B
SYN + MP_JOIN
ADD_ADDR option
SYN/ACK + MP_JOIN
ACK + MP_JOIN
??

## Slide 10: Starting a new subflow: the other way
Simultaneously, an ADD_ADDR option(5-tuple) is sent on an existing subflow, informing the receiver of the sender’s alternative address.

## Slide 11: Considering
MPTCPの問題
  性能に関して-ショートフロー問題
    ルーティングが静的
  運用に関して-IPアドレスの問題、ルーティングテーブルの問題
    原理上MPTCPは5-tuple

## Slide 12: 提案手法もどき
Conflict

## Slide 13: 提案手法もどき
Pod内の最大マッチング問題。。
Round-Robin Matching
iSLIP(1999)
Balancing!

## Slide 14: Issue of manageability
10.3.0.1
10.3.0.2
10.1.3.1
10.1.3.2
10.3.2.1
10.3.1.2
10.3.1.1
10.3.2.2
10.1.0.1
10.1.0.2
10.3.0.1
10.3.0.2
10.2.0.1
10.2.0.2
10.2.3.1
10.2.3.2

## Slide 15: Issue of manageability
10.3.0.1
10.3.0.2
10.1.3.2:port80
10.3.2.1
10.3.1.2
10.3.1.1
10.3.2.2
10.1.0.2:port80
10.3.0.1
10.3.0.2
10.1.0.2:port81
10.1.3.2:port81
NAT
NAT

## Slide 16: ステート型ルーティングプロトコル
non-accept判定は?
パスを切り替えるためには？

## Slide 17: Future work
実装
  仮想環境での2サーバ、2ルータでMPTCP on mininet
  Openflow コントローラの勉強
論文
  MPTCP + OpenFlow
  MPTCP implementation