## Slide 1: Progress report 進捗報告
Sekiya laboratory M1
Fujii Shogo

## Slide 2: 提案手法 – シナリオ
Conflict

## Slide 3: 提案手法もどき
Balancing!

## Slide 4: 提案手法 – ロードバランス
シミュレーション計画 : ショートフローの3-wayハンドシェイクがスムーズに行われれば、改善される
  0. ショートフローが遅延したのは、3-wayハンドシェイク時の遅延の影響か?(ウィンドウサイズが開かなかったから)
  ロングフローが使っている経路にショートフローを流して遅延するのか?ショートフローは別の経路に流して改善されるのか?(改善されてほしい)
  スイッチにフローが集中する事で遅延はないか?(パケットロスを起こすほどのものはない) – incast問題
  ショートフローが使う経路を適切に選択する事で、ロングフローとの衝突は避けられるか?(負荷が小さい経路を利用する事で回避)

## Slide 5: 適切に経路を選択するために…
何を基準に経路を選ぶ?
どうやって切り替える?

## Slide 6: Related work
Problem:
  Today’s data centers host online services on multiple servers. Dedicated load balancers become a single point of failure and congestion.
Solution:
  OpenFlow controller supports wildcard rules for a more scalability.
  automatically adjust to changes in load-balancing policies
Wang, Richard, Dana Butnariu, and Jennifer Rexford. "OpenFlow-based server load balancing gone wild." Proceedings of the 11th USENIX Association, 2011.

## Slide 7: Basic model from load balancer switch’s view
Each server replica R has a unique IP address and an integer weight α.
The load-balancer switch rewrites the dst IP address

## Slide 8: Proposed load-balancing solution
The switch performs :
  Rewriting the server IP address
  Forwarding the packet to the output port
How to load-balance?
  dividing client traffic based on the low-order bits.
  OpenFlow switches only support ”don’t care” bits on the lower-order bit.
Goal :
  to generate a small set of wildcard rules
  to change the wildcard rules in the target distribution of load with minimizing the number of changes.

## Slide 9: Minimizing the number of wildcard rules
(a) : simple approach does not lead to the minimum number of rules
(b) : achieving the minimum of four rules ; 0*, 10*, 110*, and 111*

## Slide 10: Transitioning for wildcard rule changes
In transition period, different connections exists until they end.
Proposed algorithm installs a microflow rule with a 60-second soft timeout

## Slide 11: Implementation and Evaluation
Experimental environment:
  OpenVswitch with NOX
  on mininet
  Web server : Mongoose
Traffic:
  sending 16MB file with 36 clients
  The division of load is relatively close to the 3:4:1 target split
  After 75 seconds, we change α2 from 4 to 0 for maintenance.

## Slide 12: Implementation and Evaluation
R2’s load eventually drops to 0 as the last few ongoing connections complete.
Initially, there were 6 wildcard rules installed, concluded with only 3 wildcard rules.

## Slide 13: 考えた事
Wildcardを用いたポリシーベースのルーティング
  IPアドレススペースといっておきながら、バイナリで話を進めたい? – 0*, 10* …
  結局、アドレスのprefixで頑張っていた
重みを用いたルーティング -> 重み=負荷として重みの小さい方へルーティング
重みをどう決めるか? : Ongoing work
  トラフィックの測定が必要
任意のネットワークでの制御?
  どうやってポリシーを収束させる?

## Slide 14: 提案手法 – ロードバランス
シミュレーション計画 : ショートフローの3-wayハンドシェイクがスムーズに行われれば、改善される
  0. ショートフローが遅延したのは、3-wayハンドシェイク時の遅延の影響か?(ウィンドウサイズが開かなかったから)
  ロングフローが使っている経路にショートフローを流して遅延するのか?ショートフローは別の経路に流して改善されるのか?(改善されてほしい)
  スイッチにフローが集中する事で遅延はないか?(パケットロスを起こすほどのものはない)
  ショートフローが使う経路を適切に選択する事で、ロングフローとの衝突は避けられるか?(負荷が小さい経路を利用する事で回避)

## Slide 15: 再現シミュレーション - 結果
完結時間の分布から4つのパターンが現れた
MPTCPはパケットロスを生じる割合が大きかった
Full window
Intensive flow
Delay with loss
Extreme delay
パケットロスが生じた

## Slide 16: 経路への負荷をどう調べる?
検討中 : αをどう決めるか?
  スイッチベースのアプローチ：
    フロー滞在時間が長い = ウィンドウサイズが拡大し負荷大
    フローの数が多い = 複数のフローが経路を共有している
    定期的にスループットを計測
  エンドホストベース：
    経路にデータが流れているかどうか

## Slide 17: Future work
実装
  仮想環境での2サーバ、2ルータでMPTCP on mininet on 64bit
  Openflow コントローラの勉強
座学
  カーネルコードを読む。
  (gdb) break mptcp_init4_subsockets等